|  |  |  | All types shall meet federal, state, and agency requirements for motor vehicle safety standards, including all gross vehicle weight ratings when fully loaded. Type 3 engines and tactical water tenders shall be equipped with a foam proportioner system. All water tenders and engines Type 3 through 6 shall be able to prime and pump water from a 10 foot lift. Personnel shall meet the qualification requirements of NWCG Wildland Fire Qualifications System Guide, PMS 310-1. |
| --- | --- | --- | --- |
|  | Engine |  |
|  | Structure Type 1 |  |
|  | Minimum Requirements |  |
| □ | Tank min. capacity (gal) | 300 |  |
| □ | Pump min. flow (gpm) | 1000 |  |
| □ | @ rated pressure (psi) | 150 |  |
| □ | Hose 2 1/2" | 1200 |  |
| □ | 1 1/2" | 500 |  |
| □ | 1" | - |  |
| □ | Equipment per NFPA 1901 | Yes |  |
| □ | Master stream 500 gpm min | Yes |  |
| □ | Pump and roll | - |  |
| □ | Maximum GVWR (lbs) | - |  |
| □ | Personnel (min) | 4 |  |
|  | Engine | All types shall meet federal, state, and agency requirements for motor vehicle safety standards, including all gross vehicle weight ratings when fully loaded. Type 3 engines and tactical water tenders shall be equipped with a foam proportioner system. All water tenders and engines Type 3 through 6 shall be able to prime and pump water from a 10 foot lift. Personnel shall meet the qualification requirements of NWCG Wildland Fire Qualifications System Guide, PMS 310-1. |
|  | Structure Type 2 |  |
|  | Minimum Requirements |  |
| □ | Tank min. capacity (gal) | 300 |  |
| □ | Pump min. flow (gpm) | 500 |  |
| □ | @ rated pressure (psi) | 150 |  |
| □ | Hose 2 1/2" | 1000 |  |
| □ | 1 1/2" | 500 |  |
| □ | 1" | - |  |
| □ | Equipment per NFPA 1901 | Yes |  |
| □ | Master stream 500 gpm min | - |  |
| □ | Pump and roll | - |  |
| □ | Maximum GVWR (lbs) | - |  |
| □ | Personnel (min) | 3 |  |
|  | Engine | All types shall meet federal, state, and agency requirements for motor vehicle safety standards, including all gross vehicle weight ratings when fully loaded. Type 3 engines and tactical water tenders shall be equipped with a foam proportioner system. All water tenders and engines Type 3 through 6 shall be able to prime and pump water from a 10 foot lift. Personnel shall meet the qualification requirements of NWCG Wildland Fire Qualifications System Guide, PMS 310-1. |
|  | Wildland Type 3 |  |
|  | Minimum Requirements |  |
| □ | Tank min. capacity (gal) | 500 |  |
| □ | Pump min. flow (gpm) | 150 |  |
| □ | @rated pressure (psi) | 250 |  |
| □ | Hose 2 1/2" | - |  |
| □ | 1 1/2" | 1000 |  |
| □ | 1" | 500 |  |
| □ | Equipment per NFPA 1901 | - |  |
| □ | Master stream 500 gpm min | - |  |
| □ | Pump and roll | Yes |  |
| □ | Maximum GVWR (lbs) | - |  |
| □ | Personnel (min) | 3 |  |
|  | Engine | All types shall meet federal, state, and agency requirements for motor vehicle safety standards, including all gross vehicle weight ratings when fully loaded. Type 3 engines and tactical water tenders shall be equipped with a foam proportioner system. All water tenders and engines Type 3 through 6 shall be able to prime and pump water from a 10 foot lift. Personnel shall meet the qualification requirements of NWCG Wildland Fire Qualifications System Guide, PMS 310-1. |
|  | Wildland Type 4 |  |
|  | Minimum Requirements |  |
| □ | Tank min. capacity (gal) | 750 |  |
| □ | Pump minimum flow (gpm) | 50 |  |
| □ | @ rated pressure (psi) | 100 |  |
| □ | Hose 2 1/2" | - |  |
| □ | 1 1/2" | 300 |  |
| □ | 1" | 300 |  |
| □ | Equipment per NFPA 1901 | - |  |
| □ | Master stream 500 gpm min. | - |  |
| □ | Pump and roll | Yes |  |
| □ | Maximum GVWR (lbs) | - |  |
| □ | Personnel (min) | 2 |  |
|  | Engine | All types shall meet federal, state, and agency requirements for motor vehicle safety standards, including all gross vehicle weight ratings when fully loaded. Type 3 engines and tactical water tenders shall be equipped with a foam proportioner system. All water tenders and engines Type 3 through 6 shall be able to prime and pump water from a 10 foot lift. Personnel shall meet the qualification requirements of NWCG Wildland Fire Qualifications System Guide, PMS 310-1. |
|  | Wildland Type 5 |  |
|  | Minimum Requirements |  |
| □ | Tank min. capacity (gal) | 400 |  |
| □ | Pump minimum flow (gpm) | 50 |  |
| □ | @ rated pressure (psi) | 100 |  |
| □ | Hose 2 1/2" | - |  |
| □ | 1 1/2" | 300 |  |
| □ | 1" | 300 |  |
| □ | Equipment per NFPA 1901 | - |  |
| □ | Master stream 500 gpm min | - |  |
| □ | Pump and roll | Yes |  |
| □ | Maximum GVWR (lbs) | 26,000 |  |
| □ | Personnel (min) | 2 |  |
|  | Engine | All types shall meet federal, state, and agency requirements for motor vehicle safety standards, including all gross vehicle weight ratings when fully loaded. Type 3 engines and tactical water tenders shall be equipped with a foam proportioner system. All water tenders and engines Type 3 through 6 shall be able to prime and pump water from a 10 foot lift. Personnel shall meet the qualification requirements of NWCG Wildland Fire Qualifications System Guide, PMS 310-1. |
|  | Wildland Type 6 |  |
|  | Minimum Requirements |  |
| □ | Tank min. capacity (gal) | 150 |  |
| □ | Pump minimum flow (gpm) | 50 |  |
| □ | @ rated pressure (psi) | 100 |  |
| □ | Hose 2 1/2" | - |  |
| □ | 1 1/2" | 300 |  |
| □ | 1" | 300 |  |
| □ | Equipment per NFPA 1901 | - |  |
| □ | Master stream 500 gpm min | - |  |
| □ | Pump and roll | Yes |  |
| □ | Maximum GVWR (lbs) | 19,500 |  |
| □ | Personnel (min) | 2 |  |
|  | Engine | All types shall meet federal, state, and agency requirements for motor vehicle safety standards, including all gross vehicle weight ratings when fully loaded. Type 3 engines and tactical water tenders shall be equipped with a foam proportioner system. All water tenders and engines Type 3 through 6 shall be able to prime and pump water from a 10 foot lift. Personnel shall meet the qualification requirements of NWCG Wildland Fire Qualifications System Guide, PMS 310-1. |
|  | Wildland Type 7 |  |
|  | Minimum Requirements |  |
| □ | Tank min. capacity (gal) | 50 |  |
| □ | Pump minimum flow (gpm) | 10 |  |
| □ | @ rated pressure (psi) | 100 |  |
| □ | Hose 2 1/2" | - |  |
| □ | 1 1/2" | - |  |
| □ | 1" | 200 |  |
| □ | Equipment per NFPA 1901 | - |  |
| □ | Master stream 500 gpm min | - |  |
| □ | Pump and roll | Yes |  |
| □ | Maximum GVWR (lbs) | 14,000 |  |
| □ | Personnel (min) | 2 |  |
|  | Water Tender Type | All types shall meet federal, state, and agency requirements for motor vehicle safety standards, including all gross vehicle weight ratings when fully loaded. Type 3 engines and tactical water tenders shall be equipped with a foam proportioner system. All water tenders and engines Type 3 through 6 shall be able to prime and pump water from a 10 foot lift. Personnel shall meet the qualification requirements of NWCG Wildland Fire Qualifications System Guide, PMS 310-1. |
|  | Support S1 |  |
|  | Minimum Requirements |  |
| □ | Tank capacity (gal) | 4000 |  |
| □ | Pump minimum flow (gpm) | 300 |  |
| □ | @ rated pressure (psi) | 50 |  |
| □ | Max. refill time (minutes) | 30 |  |
| □ | Pump and roll | - |  |
| □ | Personnel (min) | 1 |  |
|  | Water Tender Type | All types shall meet federal, state, and agency requirements for motor vehicle safety standards, including all gross vehicle weight ratings when fully loaded. Type 3 engines and tactical water tenders shall be equipped with a foam proportioner system. All water tenders and engines Type 3 through 6 shall be able to prime and pump water from a 10 foot lift. Personnel shall meet the qualification requirements of NWCG Wildland Fire Qualifications System Guide, PMS 310-1. |
|  | Support S2 |  |
|  | Minimum Requirements |  |
| □ | Tank capacity (gal) | 2500 |  |
| □ | Pump minimum flow (gpm) | 200 |  |
| □ | @ rated pressure (psi) | 50 |  |
| □ | Max. refill time (minutes) | 20 |  |
| □ | Pump and roll | - |  |
| □ | Personnel (min) | 1 |  |
|  | Water Tender Type | All types shall meet federal, state, and agency requirements for motor vehicle safety standards, including all gross vehicle weight ratings when fully loaded. Type 3 engines and tactical water tenders shall be equipped with a foam proportioner system. All water tenders and engines Type 3 through 6 shall be able to prime and pump water from a 10 foot lift. Personnel shall meet the qualification requirements of NWCG Wildland Fire Qualifications System Guide, PMS 310-1. |
|  | Support S3 |  |
|  | Minimum Requirements |  |
| □ | Tank Capacity (gal) | 1000 |  |
| □ | Pump minimum flow (gpm) | 200 |  |
| □ | @ rated pressure (psi) | 50 |  |
| □ | Max. refill time (minutes) | 15 |  |
| □ | Pump and roll | - |  |
| □ | Personnel (min) | 1 |  |
|  | Water Tender Type | All types shall meet federal, state, and agency requirements for motor vehicle safety standards, including all gross vehicle weight ratings when fully loaded. Type 3 engines and tactical water tenders shall be equipped with a foam proportioner system. All water tenders and engines Type 3 through 6 shall be able to prime and pump water from a 10 foot lift. Personnel shall meet the qualification requirements of NWCG Wildland Fire Qualifications System Guide, PMS 310-1. |
|  | Tactical T1 |  |
|  | Minimum Requirements |  |
| □ | Tank capacity (gal) | 2000 |  |
| □ | Pump minimum flow (gpm) | 250 |  |
| □ | @ rated pressure (psi) | 150 |  |
| □ | Max. refill time (minutes) | - |  |
| □ | Pump and roll | Yes |  |
| □ | Personnel (min) | 2 |  |
|  | Water Tender Type | All types shall meet federal, state, and agency requirements for motor vehicle safety standards, including all gross vehicle weight ratings when fully loaded. Type 3 engines and tactical water tenders shall be equipped with a foam proportioner system. All water tenders and engines Type 3 through 6 shall be able to prime and pump water from a 10 foot lift. Personnel shall meet the qualification requirements of NWCG Wildland Fire Qualifications System Guide, PMS 310-1. |
|  | Tactical T2 |  |
|  | Minimum Requirements |  |
| □ | Tank capacity (gal) | 1000 |  |
| □ | Pump minimum flow (gpm) | 250 |  |
| □ | @ rated pressure (psi) | 150 |  |
| □ | Max. refill time (minutes) | - |  |
| □ | Pump and roll | Yes |  |
| □ | Personnel (min) | 2 |  |

|  | Aerial (Ladder or Platform) | Designate "L" for Ladder, or "P" for Platform. |
| --- | --- | --- |
|  | Type 1-L or Type 1-P |  |
|  | Minimum Requirements |  |
| □ | Aerial | 75 ft |  |
| □ | Elevated Stream (gpm) | 500 |  |
| □ | Ground Ladders | 115 ft |  |
| □ | Personnel (min) | 4 |  |

|  | Aerial (Ladder or Platform) | Designate "L" for Ladder, or "P" for Platform. |
| --- | --- | --- |
|  | Type 2-L or Type 2-P |  |
|  | Minimum Requirements |  |
| □ | Aerial | 50 ft |  |
| □ | Elevated Stream (gpm) | 500 |  |
| □ | Ground Ladders | 115 ft |  |
| □ | Personnel (min) | 4 |  |